| Specification Section 32 31 00 2150 PEDESTRIAN SWING GATE WITH ELECTRO-MECHANICAL LOCK |  |  |
| --- | --- | --- |

GENERAL

  - SECTION INCLUDES:

    - The work in this section shall include furnishing all labor, materials, equipment and appliances necessary to complete installation of Pedestrian Swing Gate System(s) required for this project in strict accordance with this specification section and drawings.

  - REFERENCES:

    - American Welding Society AWS D1.1 / D1.1M Structural Welding Code.  See    1.04 C.

    - ASTM A 123 Standard Specification for Zinc (Hot-Dip Galvanized) Coatings on Iron and Steel.

  - SUBMITTAL:

    - Product Data:

      - Provide manufacturer’s catalog cuts with printed specifications and installation instructions.

      - Furnish detailed sequence of operation (description of system).

    - Certifications

      - The steel welders and welding process must be certified per section 1.08 A-2.

  - Pedestrian SWING GATE MANUFACTURERS:

    - The Pedestrian Swing Gate Systems shall be manufactured by Tymetal Corp., 2549 State Route 40, Greenwich, NY  12834 – (800) 328 – 4283.

    - Approved substitution – All other pedestrian swing gate systems must be submitted to the design team in accordance with substitution requirements as set forth in the general provisions of the project manual for approval prior to the bid date.  Products submitted after the bid date will not be approved.

    - Gate manufacturer shall provide independent certification as to the use of a documented Welding Procedure Specification and Procedure Qualification Record to insure conformance to the AWS D1.1 / D1.1M Structural Welding Code – Steel.  Upon request, Individual Certificates of Welder Qualification documenting successful completion of the requirements of the AWS D1.1 / D1.1M code shall also be provided.  See 1.08 A.2.

    - Store gate frames on building site, in an upright position, under cover, on wood sills or floors, and in a manner that prevents rust or damage.  Ventilate canvas or plastic covers to prevent moisture traps.

  - SYSTEM DIMENSIONS:

    - Each gate shall have a clear gate opening width of [3 feet 0 inches (0.91m] [3 feet 6 inches (1.07m)] [4 feet 0 inches (1.22m)] [5 feet 0 inches (1.52m)] and a gate height of 7 feet 0 inches (2.13m).

  - SYSTEM FUNCTION:

    - General Description:

      - Pedestrian Swing Gate System shall be designed as an exterior security swing gate.

      - The swing gate(s) shall be pre-assembled, pre-hung and tested at the manufacturer’s location.

    - Operation:

      - When the gate is in the closed position, it shall be impossible for the gate to be opened except by electrical or mechanical means.

    - Pedestrian Swing Gate Lock:

      - Gate shall be furnished with an electro-mechanical lock.  Lock requires 115V power Supply by others.

    - Self-Closing:

      - The Pedestrian Swing Gate System shall be equipped with a door closer.

    - Door Position Indication Switch:

      - The Pedestrian Swing Gate System shall be equipped with a door position switch.

  - SYSTEM COMPONENTS:

    - Security Gate Panel Filler:

      - Gate panel filler shall be ½” x 3” x 9 gauge (13 mm x 76 mm x 4 mm) weld mesh. Optional gate filler (example: chain link mesh or ornamental picket) can be added.

    - Coating:

      - The entire gate frame and door assembly shall be hot-dip galvanized after fabrication and welding.

    - Hinges:

      - Two (2) needle bearing hinges per gate shall be furnished and shall have a thrust capacity (door weight) of 600 lbs per pair.

    - Electro-mechanical Lock:

      - 115v Electro-mechanical swing gate lock, keyed both sides, shall be supplied with one key per key code.

    - Door Closer:

      - Door closer case and internal parts shall be steel and cast iron with constant viscosity liquid from 120 degrees F to -30 degrees F.  Rust inhibitor paint shall be applied.

    - Door Pulls:

      - Door pulls shall be Tymetal standard pull.

    - Door Position Indicator Switch:

      - Rotary door position switch shall be TYM – 8750/16353.

  - FABRICATION:

    - General:

      - Pedestrian Swing Gate systems shall be fully assembled at the factory and shipped to the project site ready for installation.

      - All welds on the gate frame shall conform to Welding Procedure Specification and Procedure Qualification Record to insure conformance to AWS D1.1 / D1.1M Structural Welding Code – Steel.  All individual welders shall be certified to AWS D1.1 / D1.1M welding code.  See 1.04 C.

      - Steel members shall be straight, true and free from dents, buckle, twist or rough edges.  All joints shall be tight metal-to-metal welded finish.  All welds shall show uniform section and deep penetration.  Clean weld spatter off so that surfaces are easily cleaned.

      - The entire gate frame and door assembly shall be hot-dip galvanized after fabrication and welding.

    - Frames, Stiles and Rails:

      - Steel members shall be tubular in cross-section with a minimum wall thickness of 3/16" (5mm).  Members shall be mitered and welded at the corners.

  - FINISH:

    - Galvanizing:

      - All exposed system parts shall be zinc galvanized or as otherwise specified.

EXECUTION

  - Site INSPECTION:

    - Final grades and installation conditions shall be examined.  Installation shall not begin until all unsatisfactory conditions are corrected.

  - INSTALLATION:

    - Equipment in this section shall be installed in strict accordance with the company’s printed instructions unless otherwise shown on the contract drawings.

  - SYSTEM validation:

    - The complete system shall be adjusted to assure it is performing properly.

    - The system shall be operated for a sufficient period of time to determine that the system is in proper working order.

Tymetal Corp. reserves the right to modify and/or make changes as deemed necessary without previous notice.