GENERAL:

SECTION INCLUDES:

    - This section covers the furnishing and surface installation of a TBW-4 Vehicle Barrier Wedge system. Provide complete system that has been fabricated and tested for proper operation at the factory.

    - System includes barrier plate section, power units, hydraulic cylinders, Programmable Logic Controller (PLC), and safety devices to provide a fully operational barrier system on existing concrete slab (10” depth suggested - minimum depth 8”).

RELATED SECTIONS:

    - Section 28 00 00 – Electronic Safety and Security

    - Section 32 31 00 Fencing and Gates

CRASH RATING, TESTING AND QUALITY ASSURANCE:

    - The TBW-4 vehicle barrier model is engineered to meet ASTM F2656-07 M30 (equivalent to DOS K4 rating), in which the impact conditions are:

Crash Rating		Vehicle Weight 	Impact Speed

F2656-07 M30 		15,000 lbs 		30 MPH

    - Manufacturer shall be a company specializing in the supply of security vehicle barriers.

SUBMITTALS:

    - Submit shop drawings of standard product and finish samples.

    - Indicate pertinent dimensions, general construction, component connections and location, anchorage methods and location, hardware, and installation details.

DELIVERY, STORAGE AND HANDLING:

    - Deliver material to job site in manufacturer’s packaging undamaged, compete with installation instructions.

    - Store off ground, under cover, protected from weather and construction activities.

PROJECT – SITE CONDITIONS:

    - Install TBW-4 vehicle barrier on existing concrete with minimum depth of 8” (10” suggested concrete depth) per manufacturer’s printed instructions.

    - Installer/owner to supply required permits/inspections.

WARRANTY:

    - Three (3) years from date of shipment on manufactured components and workmanship.  This warranty excludes normal wear on finishes or damage that occurs due to impact, abuse, misuse or acts of God.

    - Accessories are covered by their manufacturer’s warranty.

    - Warranty is in lieu of all other warranties, expressed or implied, and shall be considered void if visible evidence implies recommended installation procedures and maintenance instructions were not followed.

PRODUCTS:

gate system MANUFACTURERS:

    - The vehicle barrier system shall be manufactured to Tymetal Corp. specifications and shall be supplied by Tymetal Corp., 2549 State Route 40, Greenwich, NY  12834  -  (800) 328 - 4283.

    - Approved substitution – All other systems must be submitted to the design team in accordance with substitution requirements as set forth in the general provisions of the specification manual for approval prior to the bid date.  Products submitted after the bid date will not be approved.

Vehicle BARRIER:

    - The TBW-4 barrier consists of a rigid steel plate raised and lowered between two attached steel buttresses which contain the drive mechanism and controls.  The barrier unit is assembled at the factory and can be affixed to either existing concrete slabs or new concrete.  The barrier is raised and lowered by means of an electro-hydraulic power unit in 6-8 seconds for normal operation.  An optional Emergency Fast Operation (EFO) feature is available.

    - Mechanical Components:

      - Barrier plate: Constructed from steel and welded steel components. Overall plate width dimension is 8’ (standard) with 35” plate height when raised. Plate width dimensions area available up to 14’ (in 1’ increments). Barrier plate is painted red.

      - Stanchions (buttresses): Constructed of steel welded components and sheet steel. Painted red.

      - Hydraulic Cylinders: Clevis mounted between each stanchion (buttress) and the barrier plate. Clevis pins are designed to be easily removed and lubricated during normal maintenance.

    - Electrical Components:

      - Power Options: The TBW-4 unit can operate from a 120 VAC single phase power source (without Emergency Fast Operation (EFO) option).  It is also available with 208-230VAC single phase or 208-230VAC three phase, 60 Hz; 50 Hz is available.

      - Power Unit: Comprised of pump, motor and valve(s) and are housed in each of the stanchions (buttresses) along with the corresponding hydraulic cylinders. Each power unit operates a single hydraulic cylinder. Remote power unit optional

      - Control Enclosure: Constructed to NEMA 3 specifications and contains all electrical components including the PLC controller, motor, circuit breakers and the hydraulic fluid tank, associated pump and hoses/fittings required for proper operation. Prewired for optional vehicle loop detectors.

      - Auxiliary limit switches.

      - Controls: TBW-4 units require activation controls such as a card reader, keypad, push button, etc. (typically by others) for normal operation.

    - Factory Inspection and Testing:

      - Manufacturer shall test each operator at factory to assure smooth, quiet operation.

      - Manufacturer shall test all control inputs to ensure proper function.

FINISHES:

    - Barrier is delivered with zinc rich primer coating and three part epoxy paint for frame and buttresses – Standard color for the TBW-4 unit is red. Other colors available.

EXECUTION:

Site Inspection:

    - Examine final grades and installation conditions.

    - Installer must examine the location and advise the Contractor/Owner of any site conditions unacceptable for proper installation of product.  The conditions include but are not limited to the following:

      - Existing underground utilities or unforeseen issues.

      - Removal of pavers, stones road surfaces or landscaping.

    - Do not begin work until all unsatisfactory conditions are corrected.

Installation:

    - Install equipment of this section in strict accordance with the company’s printed instructions.

    - Set units level and plumb and in line with adjacent structures or roadway.  Anchor securely into place.

    - Use installers with experience in the installation of vehicle barriers.  For a list of qualified installers please contact manufacturer.

System Acceptance & validation:

    - Acceptance Test:

      - Test each system function.

      - Installer should adjust barrier, hardware and sensors for smooth operation and proper performance.

    - Test and Explain Safety Features:

      - Ensure that the owners and operator of the barrier is clear on the electrical disconnection, hydraulic depressurization and safe manual operation of the unit.

      - Ensure that all instructions for mechanical components, safety devices and installed accessories are available for everyone who will be using the vehicle barrier system.

    - System Validation:

      - The complete system shall be adjusted to assure it is performing properly.

      - The system shall be operated for a sufficient period of time to determine that the system is in proper working order.

      - Ensure the owner is clear with regard to the safety points concerning the basic operational guidelines of the vehicle barrier system.

      - Installer and customer shall complete Post Installation Check Off Sheet.

Note: Tymetal Corp. reserves the right to modify and/or make changes as deemed necessary without previous notice.